OMB Control No. xxxx-xxxx

Inspection Checklist for ENERGY STAR Qualified Modular Home – Performance Path

| Home Address: _____________________________________________________________________________________________ City: _____________________________________________ State: ______ Zip: _________ Home ID: ______________________ Instructions: Write your initials in each applicable box. If an item does not apply to the home, write “n/a”. Raters should attempt to inspect as many critical items as possible but may delegate a builder’s representative to verify and initial up to six (6) Thermal Bypass items (numbered items on the first page of this checklist). If the builder verifies any item, they must sign the second page of this checklist. Every line must contain at least one set of initials or “n/a”. |
| --- |
| Thermal Bypass Item | Inspection Guidelines | Plant QC | Rater |
|  |  | Pass | Pass | Fail |
| Overall Air Barrier and Thermal Barrier Alignment | General requirements: Insulation shall be installed in full contact with sealed interior and exterior air barrier except for alternate to interior air barrier under walls adjoining exterior walls or unconditioned spaces (see below). |
|  | All climate zones: |
|  | Overall alignment throughout home | _________ | _________ | _________ |
|  | Garage band joist air barrier (at bays adjoining conditioned space) | _________ | _________ | _________ |
|  | Attic eave baffles where vents/leakage exist | _________ | _________ | _________ |
|  | Only at Climate Zones 4 and higher: |
|  | Slab-edge insulation (Up to 25% of the slab edge may be uninsulated in Climate Zones 4 and 5.) | _________ | _________ | _________ |
|  | Best practices encouraged, not required: |
|  | Air barrier at all band joists (Climate Zones 4 and higher) | _________ | _________ |  |
|  | Minimize thermal bridging (e.g., OVE framing, SIPs, ICFs) | _________ | _________ |  |
| Walls Adjoining Exterior Walls or Unconditioned Spaces | General requirements: Fully insulated wall aligned with air barrier at both interior and exterior, OR Alternate for Climate Zones 1 thru 3, sealed exterior air barrier aligned with RESNET Grade 1 insulation fully supported Continuous top and bottom plates or sealed blocking |
|  | Wall behind shower/tub | _________ | _________ | _________ |
|  | Wall behind fireplace | _________ | _________ | _________ |
|  | Insulated attic slopes/walls | _________ | _________ | _________ |
|  | Attic knee walls | _________ | _________ | _________ |
|  | Skylight Shaft Walls | _________ | _________ | _________ |
|  | Wall adjoining porch roof | _________ | _________ | _________ |
|  | Staircase walls | _________ | _________ | _________ |
|  | Double walls | _________ | _________ | _________ |
| Floors between Conditioned and Exterior Spaces | General requirements: Air barrier is installed at any exposed insulation edges Insulation is installed to maintain permanent contact with sub-floor above |
|  | Insulated floor above garage | _________ | _________ | _________ |
|  | Cantilevered floor | _________ | _________ | _________ |
| Shafts | General requirements: Openings to unconditioned space are fully sealed with solid blocking or flashing and any remaining gaps are sealed with caulk or foam (provide fire-rated collars and caulking where required) |
|  | Duct shaft | _________ | _________ | _________ |
|  | Piping shaft/penetrations | _________ | _________ | _________ |
|  | Flue shaft | _________ | _________ | _________ |
| Attic / Ceiling Interface | General requirements: All attic penetrations and dropped ceilings include a full interior air barrier aligned with insulation with any gaps fully sealed with caulk, foam or tape Movable insulation fits snugly in opening and air barrier is fully gasketed |
|  | Attic access panel (fully gasketed and insulated) | _________ | _________ | _________ |
|  | Attic drop-down stair (fully gasketed and insulated) | _________ | _________ | _________ |
|  | Dropped ceiling/soffit (full air barrier aligned with insulation) | _________ | _________ | _________ |
|  | Recessed lighting fixtures (ICAT labeled and sealed to drywall) | _________ | _________ | _________ |
|  | Whole-house fan (insulated cover gasketed to the opening) | _________ | _________ | _________ |
| Common Walls Between Dwellings | General requirements: Gap between drywall shaft wall (common wall) and structural framing between units is sealed at all exterior boundary conditions |
|  | Common wall between dwelling units | _________ | _________ | _________ |

|  |  | Home ID: ______________________ |
| --- | --- | --- |
| Performance Path Item | Inspection Guidelines | Plant QC | Rater |
|  |  | Pass | Pass | Fail |
| Performance Index | All performance path construction specifications have been adhered to and the home has achieved the required performance index. 2004 IRC Climate Zones 1 – 5: Maximum HERS Index 85 2004 IRC Climate Zones 6 – 8: Maximum HERS Index 80 | _________ | _________ | _________ |
| Ductwork | General requirements: |
|  | Leakage ≤ 6 cfm to outdoors per 100 sq. ft. of conditioned floor area | _________ | _________ | _________ |
|  | Ducts in unconditioned spaces wrapped with R-6 minimum insulation | _________ | _________ | _________ |
|  | All exterior ducts have been mechanically secured and supported off the ground | _________ | _________ | _________ |
| ENERGY STAR Qualified Products | General requirements: Include at least one (1) of the following ENERGY STAR qualified product categories: |
|  | Heating or cooling equipment OR Windows OR Water heating equipment OR Five (5) or more qualified light fixtures, appliances, ceiling fans equipped with lighting fixtures and/or ventilation fans. | Specify: | _________ | _________ | _________ |
| Marriage Line Seal | General requirements: All vertical and horizontal marriage line areas filled with continuous non-porous insulating gaskets creating a permanent air barrier at joints in the ceiling, walls and floor. Gaskets may be one or two-part systems, including proprietary gaskets, foams, insulation wrapped in poly, or insulation covered by butyl or other long-life tape on one side. No visible signs of gaps or tears are permitted. | _________ | _________ | _________ |
| Floors over Unconditioned Spaces | General requirements: Air barrier between floor and unconditioned crawlspace is continuous and sealed. | _________ | _________ | _________ |
| Plant QC Date: _______________________________ Company: ___________________________ Signature: ___________________________ Initials:______________________________ | Rater Date: _______________________________ Company: ___________________________ Signature: ___________________________ Initials:______________________________ | Builder Date: _________________________________ Company: _____________________________ Signature: _____________________________ Initials:________________________________ |

EPA Form 5900-192

The government estimates the average time needed to fill out this form is 0.50 hours and welcomes suggestions for reducing this effort. Send comments (referencing OMB Control Number) to the Director, Collection Strategies Division, U.S. EPA (2822T), 1200 Pennsylvania Ave., NW, Washington, D.C. 20460.

# Footnotes

On-site power generation may not be used to decrease the HERS Index to qualify for ENERGY STAR.  A maximum of 20% of all screw-in light bulb sockets in the home may use compact fluorescent lamps (CFLs) to decrease the HERS Index for ENERGY STAR compliance.  CFLs used for this purpose must be ENERGY STAR qualified.

For more information, see “ENERGY STAR Qualified Homes Codes and Standards Information.”